Here's how you can set up your ATmega8A with a bootloader and then use it to upload code multiple times without needing an external Arduino:

### Step 1: Burn the Bootloader Using an External Arduino
1. **Set Up the Arduino as ISP**:
   - Connect an Arduino (e.g., Arduino Uno) to your computer.
   - Open the Arduino IDE.
   - Load the "ArduinoISP" sketch from the examples (`File > Examples > ArduinoISP`).
   - Upload this sketch to the Arduino. This turns the Arduino into an In-System Programmer (ISP).

2. **Connect the Arduino ISP to the ATmega8A**:
   - Connect the Arduino to the ATmega8A as follows:
     - **Arduino Pin 10** → **ATmega8A RESET (Pin 1)**
     - **Arduino Pin 11** → **ATmega8A MOSI (Pin 17)**
     - **Arduino Pin 12** → **ATmega8A MISO (Pin 18)**
     - **Arduino Pin 13** → **ATmega8A SCK (Pin 19)**
     - **Arduino GND** → **ATmega8A GND (Pin 8 or 22)**
     - **Arduino 5V** → **ATmega8A VCC (Pin 7 or 20)**

3. **Burn the Bootloader**:
   - In the Arduino IDE, go to `Tools > Board` and select "ATmega8" (with MiniCore installed, you'll see ATmega8 options).
   - Set the clock frequency and other options according to your setup.
   - In `Tools > Programmer`, select "Arduino as ISP."
   - Click `Tools > Burn Bootloader`. This uploads the bootloader to your ATmega8A, making it ready for serial programming via the USB-to-TTL adapter.

### Step 2: Upload Code via USB-to-TTL Adapter
1. **Connect the USB-to-TTL Adapter**:
   - Connect your USB-to-TTL adapter to the ATmega8A:
     - **TX of the adapter** → **RX of the ATmega8A (Pin 2)**
     - **RX of the adapter** → **TX of the ATmega8A (Pin 3)**
     - **GND of the adapter** → **GND of the ATmega8A (Pin 8 or 22)**
     - **VCC of the adapter** → **VCC of the ATmega8A (Pin 7 or 20)**
     - **DTR or RTS of the adapter** (if available) → **RESET of the ATmega8A (Pin 1)** (through a 100nF capacitor).

2. **Upload Code**:
   - Open the Arduino IDE.
   - Write or open your code (sketch).
   - Select the appropriate board (ATmega8 with the correct clock settings).
   - In `Tools > Port`, select the COM port associated with your USB-to-TTL adapter.
   - Click `Upload`. The bootloader will handle the process, allowing your code to be uploaded to the ATmega8A.

### Step 3: Repeat Code Uploads
- Now, each time you want to upload new code, you can directly use the USB-to-TTL adapter. The bootloader on the ATmega8A will automatically handle the code upload process, and there's no need to use the external Arduino again.

This setup allows you to easily and repeatedly upload code to your ATmega8A, making the development process more efficient.

If your USB-to-TTL adapter doesn’t have a DTR (Data Terminal Ready) pin, you can manually reset the ATmega8A to trigger the bootloader when uploading code. Here’s how you can do it using a button:

### Step 1: Wire the Button for Manual Reset
1. **Connect the Reset Pin**:
   - Connect one leg of your push button to the **RESET** pin of the ATmega8A (Pin 1).
   - Connect the other leg of the button to **GND**.

2. **Pull-up Resistor**:
   - Connect a 10kΩ resistor between the **RESET** pin (Pin 1) and **VCC** (Pin 7 or 20). This pull-up resistor keeps the microcontroller running normally when the button is not pressed.

### Step 2: Manual Reset During Code Upload
1. **Prepare to Upload Code**:
   - Write or open your code (sketch) in the Arduino IDE.
   - Select the correct board settings (ATmega8 with the appropriate clock and bootloader).
   - Select the correct COM port for your USB-to-TTL adapter.

2. **Trigger the Bootloader**:
   - Click the **Upload** button in the Arduino IDE.
   - Immediately after clicking **Upload**, press and hold the reset button on your ATmega8A.
   - Release the button just as you see the "Uploading..." message in the Arduino IDE. This manual reset puts the ATmega8A into bootloader mode, ready to receive the new code.

3. **Code Upload**:
   - The code should upload successfully if the timing of the reset is correct.

### Step 3: Repeat the Process
- Each time you upload new code, you’ll need to manually reset the ATmega8A at the right moment to trigger the bootloader.

This manual reset method is a common workaround when your USB-to-TTL adapter lacks a DTR pin. It may take a few tries to get the timing just right, but it works reliably once you get the hang of it.